English version

Municipal Enterprise “Urban Bus Park” (in Romanian language: “Parcul urban de autobuze”) invites economic entities with a status of resident or non-resident companies to make propositions that can meet the needs of the company regarding supply of 100 buses as per the following technical specifications:

1. Purpose – bus for transportation of persons within the urban area

2. Production year - 2006-2012

3. Capacity - 90-120 persons

4. Number of seating places - 20-.35

5. Length – up to 16000 mm

6. Width – not more than 2550 mm

7. Height – not more than 3000 mm

8. Number of doors - 3-4, door width – at least 1300 mm (except without door)

9. Floor level – low floor across the entire bus length

10. Floor arrangement – non-slippery material.

11. Driver’s seat must be equipped with cushions and soft back, adjustable by height and distance from the steering wheel. Seat back must be adjustable by angle.

12. Rear view mirrors must be heated.

13. Driver’s cabin isolated from the salon.

14. Bus salon must be equipped with a maximum number of bars that ensure safe transportation of passengers.

15. For proper ventilation during summer the bus must be equipped with ventilation and vents.

16. Bus frame must be made of anti-corrosive metal on the entire area.

17. Non-metal materials used for improvement of the salon must not present fire danger.

18. Engine :

a) power - over 160 kW

b) toxic requirements - EURO 4

c) fuel type :

- compressed natural gas (CNG)

- diesel + CNG

19. Gear box :

a) type - automatic

b) number of gears - 4+1

20. Braking system - pneumatic with ABS

21. Rear foot bridge – similar to RABA

22. Auxiliary equipment:

a) control device EG (tachograph)

b) electronic information system (front, back, lateral)

c) communication system (digital communication device)

d) tires – similar to “MATADOR”

23. Furnishing must provide for: first aid kit, jack, instruments, spare tire and emergency sign, operation, maintenance and repair manual must be available in each bus. For purpose of improvement of fire safety the bus must be equipped with fire extinguishers installed in easily accessible places.

24. The bus must be equipped with access bridges for locomotor system handicapped persons.

25. Warranty period - 12 month or 100 thousand km.

26. Price - 1 bus up to 30,000 Euro.

27. During the warranty period the supplier must ensure replacement of defective parts at his own expense.

Interested economic entities are invited to receive more information and send their offers until 30.11.2012 to: Republic of Moldova, MD-2032, Chisinau city 51, Sarmizegetusa street, tel/fax+373 22/ 55-60-30. E-mail directorpua@gmail.com .